## Slide 1: Diverter Math
Finding Diverts Based on Start and End Points

## Slide 2: Function Blocks
AsmGetSegment
  Iterates through every segment reference
SegGetInfo
  Needs a segment reference
  Gives information about a segment
    Thing of use: Start Point and End Point

## Slide 3: Start Point and End Point
Pos (X, Y, and Z)
Orientation (3 angles)
  3rd angle is about z which is what we need
  Oddity for angles 1 and 2:
  Points facing down, left, or up
    Angle 1 is 0 and angle 2 is 180
  Points facing right and down to but not including straight down
    Angle 1 is 0 and angle 2 is -180
  Points facing up to but not including straight up and over to the right but not including right
    Angle 1 is 180 and angle 2 is 0
Function Blocks
-180
90
0
-90
-45
45
135
45
22.5
67.5

## Slide 4: Start Point and End Point
  To make them all in the same useful coordinate system:
  Angle 1 is 0 and angle 2 is 180
    Transform by taking absolute value
  Angle 1 is 0 and angle 2 is -180
    Transform by +360
  Angle 1 is 180 and angle 2 is 0
    Transform by +180
Function Blocks
-180
90
0
-90
-45
45
135
45
22.5
67.5
180
90
0
270
315
45
135
225
202.5
247.5

## Slide 5: Points
By keeping the points within the segment info structure, I can keep the points connected to each other based on segments they belong to
  Builds a sort of web

## Slide 6: Concept
Pick a segment
  Skip arc segments since they can never be diverts
Iterate through all other segments
  Skip arc segments since they can never be diverts
  See if a segment’s two points match up with the selected segment’s two points in a way that indicates a divert
Deciding Diverts

## Slide 7: Rules
Must happen along flat sections
Must overlap at least 90mm
  Multiple of 15mm (+-0.25mm)
Overlaps must be parallel
Must be separated by 30mm perpendicular to direction of the shuttle motion
Deciding Diverts

## Slide 8: Rules
For simplicity, multi segment diverts will be counted as multiple diverts
  I.e. A divert is only two segments
Deciding Diverts

## Slide 9: Types
There are only 3 segment types that can be used to divert, so there are only 6 unique combinations of two segments
AA – AA
AA – AB
AA – BA
AB – AB
AB – BA
BA – BA
Deciding Diverts

## Slide 10: Building a “Map”
Take AB – AB divert as an example
  Must be between 90-105mm overlap and 30mm apart
  Start 2 must be 94.87-109.20mm from Start 1 and 346.77-361.53mm from End 1
  End 2 must be 346.77-361.53mm from Start 1 and 792.83-807.73mm from End 1
Deciding Diverts
End 2
Start 1
Start 2
End 1
Y
X

## Slide 11: Building a “Map”
Building a map from these rules shows a very small range that a segment can exist in that counts as a divert
  Orange represents the segment with Start 1 and End 1
  Dark green represents where Start 2 can exist
  Dark blue represents where End 2 can exist
  Any correctly placed segment that is not a divert can not exist in this range
NOTE: We can also check the orientation of segment 2 to confirm it is 180 degrees from segment 1
Deciding Diverts

## Slide 12: Building a “Map”
Some maps, like AA-AA, won’t be exclusive enough with just knowing the distances between points
  A segment could correctly be configured 90-570mm away with the right orientation and not be a divert
AA segments form a line parallel with the divert, and any segment diverting from or to the AA will have a point 30 mm from the AA segment
The distance between a point and a line can be calculated:
  ,
  We can add an extra restriction of needing to be 30mm from the AA segment
Deciding Diverts
End 1
End 2
Start 1
Start 2

## Slide 13: Results
Maps and Rules

## Slide 14: AA-AA Diverts
Maps and Rules
Y
X
  Must overlap at least 90mm (+/-0.25mm) and be 30mm apart
  Start 2 must be 94.631-1230.616 mm from Start 1 and 30-571.039 mm from End 1
  End 2 must be 30-571.039 mm from Start 1 and 94.631-1230.616 mm from End 1
  Start 2 must be 30mm from the line formed by Start 1 and End 1
End 1
End 2
Start 1
Start 2

## Slide 15: AA-AB Diverts
Maps and Rules
Y
X
  Must overlap at least 90mm (+/-0.25mm) and be 30mm apart
  Start 2 must be 94.631-675.916mm from Start 1 and 30-571.039mm from End 1
  End 2 must be 62.683-362.647mm from Start 1 and 436.216-1019.119mm from End 1
  Start 2 must be 30mm from the line formed by Start 1 and End 1
End 1
End 2
Start 1
Start 2

## Slide 16: AA-BA Diverts
Maps and Rules
Y
X
  Must overlap at least 90mm (+/-0.25mm) and be 30mm apart
  Start 2 must be 436.216-1019.119mm from Start 1 and 62.683-362.647mm from End 1
  End 2 must be 30-571.039mm from Start 1 and 94.631-675.916mm from End 1
  End 2 must be 30mm from the line formed by Start 1 and End 1
End 1
End 2
Start 1
Start 2

## Slide 17: AB-AB Diverts
Maps and Rules
End 2
Start 1
Start 2
End 1
Y
X
  Must be between 90-105mm overlap (+/-0.25mm) and 30mm apart
  Start 2 must be 94.631-109.442mm from Start 1 and 347.391-362.647mm from End 1
  End 2 must be 347.391-362.647mm from Start 1 and 794.373-809.763mm from End 1

## Slide 18: AB-BA Diverts
Maps and Rules
End 1
End 2
Start 1
Start 2
Y
X
  Must be aligned at the gap +-15mm (+/-0.25mm) and 30mm apart
  Start 2 must be 436.216-466.420mm from Start 1 and 95.366-96.578mm from End 1
  End 2 must be 30-33.654mm from Start 1 and 436.216-466.420mm from End 1

## Slide 19: BA-BA Diverts
Maps and Rules
End 2
Start 1
Start 2
End 1
Y
X
  Must be between 90-105mm overlap (+/-0.25mm) and 30mm apart
  Start 2 must be 794.373-809.763mm from Start 1 and 347.391-362.647mm from End 1
  End 2 must be 347.391-362.647mm from Start 1 and 94.631-109.442mm from End 1

## Slide 20: Finding Good Measurement Spots
Where to Send the Shuttle

## Slide 21: Assumptions
The user will have created sectors so that every divert has at least one sector through it
Based on previous slides, all diverts are known
All diverts are configured with 30mm gaps
Finding Measurement Spots

## Slide 22: Step 1: Determine Overlap
Measurement varies based on the divert pairing
AA – AA
AA – AB
AA – BA
AB – AB
AB – BA
BA - BA
Finding Measurement Spots

## Slide 23: AA – AA
Pythagorean Theorum
Use the start point of the reference segment
Use the start point of the opposing segment
Hypotenuse is the distance between the two
  I made a FUB for this
Vertical side is 30 mm gap
Horizontal side =
If Horizontal > 660
  Overlap = 1320 – Horizontal
If Horizontal <= 660
  Overlap = Horizontal
Step 1: Determine Overlap
D
30
D
30

## Slide 24: AA – AB
Pythagorean Theorum
Use the start point of the AA segment
Use the start point of the AB segment
Hypotenuse is the distance between the two
  I made a FUB for this
Vertical side is 30 mm gap
Horizontal side =
If Horizontal >= 660
  The AB is at or past the end of the AA
  Overlap = 150 - (Horizontal – 660)
If 105 < Horizontal < 660
  The AB is in the middle of the AA
  Overlap = 105
If Horizontal <= 105
  The AB is nearing the start of the AA
  Overlap = Horizontal
Step 1: Determine Overlap
D
30
D
30
D
30
D
30

## Slide 25: AA – BA
Pythagorean Theorum
Use the end point of the AA segment
Use the end point of the AB segment
Hypotenuse is the distance between the two
  I made a FUB for this
Vertical side is 30 mm gap
Horizontal side =
If Horizontal >= 660
  The BA is at or past the start of the AA
  Overlap = 150 - (Horizontal – 660)
If 105 < Horizontal < 660
  The BA is in the middle of the AA
  Overlap = 105
If Horizontal <= 105
  The BA is nearing the end of the AA
  Overlap = Horizontal
Step 1: Determine Overlap
D
30
D
30
D
30
D
30

## Slide 26: AB – AB
Pythagorean Theorum
Use the start point of the AB segment
Use the start point of the AB segment
Hypotenuse is the distance between the two
  I made a FUB for this
Vertical side is 30 mm gap
Horizontal side =
Overlap = Horizontal
Step 1: Determine Overlap
D
30

## Slide 27: AB – BA
Pythagorean Theorum
Use the start point of the AB segment
Use the end point of the BA segment
Hypotenuse is the distance between the two
  I made a FUB for this
Vertical side is 30 mm gap
Horizontal side =
Overlap = 105 – Horizontal
Step 1: Determine Overlap
D
30
D
30
D
30

## Slide 28: BA – BA
Pythagorean Theorum
Use the end point of the BA segment
Use the end point of the BA segment
Hypotenuse is the distance between the two
  I made a FUB for this
Vertical side is 30 mm gap
Horizontal side =
Overlap = Horizontal
Step 1: Determine Overlap
D
30

## Slide 29: Step 2: Determine Middle of Overlap
Should be similar to the overlap calculation
Need a result with respect to each segment
  i.e. pos x on segX and position y on segY
Finding Measurement Spots

## Slide 30: AA – AA
Pythagorean Theorum
Use the start point of the reference segment
Use the start point of the opposing segment
Hypotenuse is the distance between the two
  I made a FUB for this
Vertical side is 30 mm gap
Horizontal side =
If Horizontal > 660
  Overlap = 1320 – Horizontal
  Reference DivMid = 660-(Overlap/2)
  Other DivMid = 660-(Overlap/2)
If Horizontal <= 660
  Overlap = Horizontal
  Reference DivMid = (Overlap/2)
  Other DivMid = (Overlap/2)
Step 2: Determine Middle of Overlap
D
30
D
30

## Slide 31: AA – AB
Pythagorean Theorum
Use the start point of the AA segment
Use the start point of the AB segment
Hypotenuse is the distance between the two
  I made a FUB for this
Vertical side is 30 mm gap
Horizontal side =
If Horizontal >= 660
  The AB is at or past the end of the AA
  Overlap = 150 - (Horizontal – 660)
  AA DivMid = 660 – (Overlap/2)
  AB DivMid = (Horizontal – 660) + (Overlap/2)
If 105 < Horizontal < 660
  The AB is in the middle of the AA
  Overlap = 105
  AA DivMid = Horizontal – 52.5
  AB DivMid = 52.5
If Horizontal <= 105
  The AB is nearing the start of the AA
  Overlap = Horizontal
  AA DivMid = (Overlap/2)
  AB DivMid = (Overlap/2)
Step 2: Determine Middle of Overlap
D
30
D
30
D
30
D
30

## Slide 32: AA – BA
Pythagorean Theorum
Use the end point of the AA segment
Use the end point of the AB segment
Hypotenuse is the distance between the two
  I made a FUB for this
Vertical side is 30 mm gap
Horizontal side =
If Horizontal >= 660
  The AB is at or past the end of the AA
  Overlap = 150 - (Horizontal – 660)
  AA DivMid = (Overlap/2)
  AB DivMid = 450 – ((Horizontal – 660) + (Overlap/2))
If 105 < Horizontal < 660
  The AB is in the middle of the AA
  Overlap = 105
  AA DivMid = 660 – (Horizontal – 52.5)
  AB DivMid = 397.5
If Horizontal <= 105
  The AB is nearing the start of the AA
  Overlap = Horizontal
  AA DivMid = 660 – (Overlap/2)
  AB DivMid = 450 – (Overlap/2)
Step 2: Determine Middle of Overlap
D
30
D
30
D
30
D
30

## Slide 33: AB – AB
Pythagorean Theorum
Use the start point of the reference segment
Use the start point of the other segment
Hypotenuse is the distance between the two
  I made a FUB for this
Vertical side is 30 mm gap
Horizontal side =
Overlap = Horizontal
Reference DivMid = (Overlap/2)
Other DivMid = (Overlap/2)
Step 2: Determine Middle of Overlap
D
30

## Slide 34: AB – BA
Pythagorean Theorum
Use the start point of the AB segment
Use the end point of the BA segment
Hypotenuse is the distance between the two
  I made a FUB for this
Vertical side is 30 mm gap
Horizontal side =
Overlap = 105 – Horizontal
Reference DivMid = (Overlap/2)
Other DivMid = 450 – (Overlap/2)
Step 2: Determine Middle of Overlap
D
30
D
30
D
30

## Slide 35: BA – BA
Pythagorean Theorum
Use the end point of the reference segment
Use the end point of the other segment
Hypotenuse is the distance between the two
  I made a FUB for this
Vertical side is 30 mm gap
Horizontal side =
Overlap = Horizontal
Reference DivMid = 450 – (Overlap/2)
Other DivMid = 450 – (Overlap/2)
Step 2: Determine Middle of Overlap
D
30

## Slide 36: Step 3: Determine Center of Divert
We know the start points and angles, end points and angles, overlap lengths, and midpoints of overlaps on segments.
Displaying in Paper

## Slide 37: Reminder of Coordinate System
  To make them all in the same useful coordinate system:
  Angle 1 is 0 and angle 2 is 180
    Transform by taking absolute value
  Angle 1 is 0 and angle 2 is -180
    Transform by +360
  Angle 1 is 180 and angle 2 is 0
    Transform by +180
Function Blocks
-180
90
0
-90
-45
45
135
45
22.5
67.5
180
90
0
270
315
45
135
225
202.5
247.5

## Slide 38: AA – AA
Base it on the reference segment
In the trak coordinate system, 0 degrees rotation is down
Overlap is known (relative to the start point)
  For BA, subtract 450 to make it relative to end point
Center of divert is 15mm from midpoint
  Makes a right angle with the overlap
Without rotation
  AA & AB
    X is startX – Overlap
    Y is startY – 15mm
  BA
    X is startX + Overlap
    Y is startY – 15mm
Step 3: Determine Center of Divert

## Slide 39: AA – AA
Most segments will be rotate by some angle
In SVGs, you can create a rectangle with the following parameters
  X
    Coordinate of the top left corner
    AA & AB: StartX – Midpoint – (Overlap/2)
    BA: EndX + (450 – midpoint) – (Overlap/2)
  Y
    Coordinate of the top left corner
    AA & AB: StartY
    BA: EndY
  Width
    Overlap
  Height
    30mm
Step 3: Determine Center of Divert

## Slide 40: AA – AA
Most segments will be rotate by some angle
In SVGs, you can rotate shapes by an angle about the point X,Y
  Angle
    Calculated as described a few slides ago
  X
      AA & AB: StartX
    BA: EndX
  Y
      AA & AB: StartY
    BA: EndY
Step 3: Determine Center of Divert

## Slide 41: Output to the User
What they need to know

## Slide 42: What we already have
  Divert Info
  Midpoint of the overlap for each segment
  A shuttle in the divert within some distance of the midpoint
  ShReadSeg
    Outputs the shuttle’s actual position on each segment
  The difference between the respective midpoints and positions can be calculated
  Shown in red
  If the segments are perfectly aligned, then the difference between these is zero
  If the segments are offset, the difference is nonzero
Output to the user

## Slide 43: Interpreting the values
  Difference between offsets
  A difference of zero mean the segments are aligned in real life exactly as they are defined in the assembly config
  A non-zero difference means the segments are slightly off from the alignment defined in the assembly config
Output to the user

## Slide 44: Interpreting the values
X
Y
  Example
  The divert midpoint on SEG_1 is at position X
    The offset of the shuttle position on SEG_1 from X is Dx
  The divert midpoint on SEG_2 is at position Y
    The offset of the shuttle position on SEG_2 from Y is Dy
  The absolute value of the difference is the alignment error, E
    |Dx – Dy| = E
Output to the user
SEG_1
SEG_2
Dy
Dx
E

## Slide 45: Interpreting the values
X
Y
  Example
  The assembly config says
    A position on SEG_1 aligns with a position on SEG_2
  Two options (user must decide)
Output to the user
SEG_1
SEG_2
Dy
Dx
E